RoboCupJunior Rescue Maze 2024

Team Description Paper
Team Repeton

Abstract
Our robot can explore a maze full of obstacles to save numerous lives. It can overcome obstacles up to 2 centimeters in height thanks to its large knobby wheels and powerful traction. This robot is built to navigate, analyze, and store information about each tile of the maze. It’s the first time that an educational microprocessor, such as the mBot-2, is being used to participate in this competition. The robot is equipped with various sensors that provide it with vital signals. This input is processed to make the best decisions according to its primary goal. Utilizing proportional control, the robot maintains a straight axis while navigating the maze, ensuring precise movements. Thanks to the data acquired during navigation, once the maze is fully explored, our robot can find the shortest path back to its starting tile. It can save lives thanks to its extremely accurate artificial intelligence, processing hundreds of images every minute to identify victims.
1. Introduction
  1. Team
- Antonio Saboanu – Captain – Software Designer: Antonio developed the main software ideas for the robot. He studies IT at school, and this is his first time participating in this type of competition. His contributions include designing the software architecture and coding key algorithms.
- Leonardo Padovan – Co-Captain – Programmer: Leonardo studied the hardware components of the robot and programmed its movements. Last year, he participated in the RoboCup Soccer competition, bringing valuable experience to our team. His expertise ensured smooth hardware-software integration.
- Matteo Finotto – Hardware Designer: Matteo ensured proper communication between the robot's components. He designed the optimal structure for cable management and selected the best components based on price, performance, and suitability for our goals. Matteo also participated in the RoboCup Soccer competition last year, contributing his experience to our project. His contributions were crucial for the robot’s hardware reliability.
- Matteo Uvaldi – 3D Designer: Matteo built the robot's structure. Leveraging his knowledge of 3D modeling, he printed custom parts that provided the best solutions to our design challenges. Last year, he participated in the RoboCup Maze competition, bringing valuable insights to our team. His work was vital for the robot’s physical assembly and durability.
#### 2. Project Planning
#### a. Overall Project Plan
Objective: Our team's objective for the competition is to build a robot capable of navigating a maze to search for victims. The robot should explore as much of the maze as possible, identify and deliver rescue kits to victims, avoid black floor areas, navigate obstacles, and find its way back to the starting point to earn bonus points.
Requirements and Constraints:
1. Physical Constraints:
  1. The robot must be able to navigate through tiles with obstacles up to 2 centimeters in height.
  2. It must avoid areas with black floors.
2. Time Constraints:
  1. The project must be completed within the competition timeline.
  2. Specific milestones and deadlines must be met to ensure timely completion.
3. Competition Rules:
  1. The robot will be awarded points based on the victims detected and obstacles navigated.
  2. It should be able to deliver rescue kits to victims.
  3. Points are awarded for correctly navigating ramps, checkpoints, speed bumps, and stairs.
  4. The robot should return to the starting point after exploring the maze for an exit bonus.
Overall Project Plan:
Key Milestones and Schedule:
1. Initial Planning and Design (Week 1-2):
  1. Team Meeting and Role Assignment (Week 1): Assign roles and responsibilities to each team member.
  2. Requirements Analysis (Week 1): Define the project requirements and constraints.
  3. Preliminary Design (Week 2): Develop initial design ideas for both hardware and software.
2. Hardware Development (Week 3-4):
  1. Component Selection (Week 3): Select appropriate components for the robot.
  2. Hardware Assembly (Week 4): Assemble the robot and ensure proper communication between components.
  3. Team Member: Matteo Finotto (Hardware Designer)
3. Software Development (Week 5-6):
  1. Algorithm Design (Week 5): Develop algorithms for navigation, victim detection, and decision-making.
  2. Programming (Week 6): Implement the software on the microprocessor.
  3. Team Members: Antonio Saboanu (Software Designer), Leonardo Padovan (Programmer)
4. 3D Design and Printing (Week 7):
  1. 3D Modeling (Week 7): Design and print custom parts needed for the robot.
  2. Team Member: Matteo Uvaldi (3D Designer)
5. Integration and Testing (Week 8-10):
  1. System Integration (Week 8): Integrate hardware and software components.
  2. Initial Testing (Week 9): Conduct preliminary tests to ensure all components work together.
  3. Iteration and Refinement (Week 10): Refine the system based on test results.
6. Final Testing and Calibration (Week 11-12):
  1. Final Testing (Week 11): Test the robot in a maze environment to ensure it meets competition requirements.
  2. Calibration and Optimization (Week 12): Optimize performance and calibrate sensors.
Project Gates:
- Gate 1 (End of Week 2): Review initial design and ensure feasibility.
- Gate 2 (End of Week 6): Review hardware and software development progress.
- Gate 3 (End of Week 10): Review integration and initial testing results.
- Gate 4 (End of Week 12): Final review before competition.
Agreement on Schedule/Plan: The team agreed on the schedule through collaborative discussions, analyzing task and competition constraints. We decided to build the mechanical robot first to have a physical platform for software testing. Each iteration will test different conditions such as obstacle navigation, victim detection, and system integration. Past performance will impact subsequent iterations by informing necessary adjustments and refinements.
#### b. Integration Plan
Integration of Solution:
1. Component Integration:
  1. Hardware Components: Assembled by Matteo Finotto, ensuring smooth communication between sensors, microprocessor, and actuators.
  2. 3D Printed Parts: Designed by Matteo Uvaldi to provide structural support and optimal component placement.
  3. Software Algorithms: Developed by Antonio Saboanu and Leonardo Padovan to control navigation, victim detection, and decision-making.
2. Communication Between Components:
  1. Microprocessor (mBot-2): Central hub for processing inputs from sensors and controlling outputs to motors and actuators.
  2. Sensors: Provide data on obstacles, victims, and floor color, which is processed to make navigation decisions.
  3. Actuators: Receive commands from the microprocessor to move the robot and deliver rescue kits.
Illustrations and Diagrams:
- Diagram 1: Overall system architecture showing the microprocessor, sensors, and actuators.
- Diagram 2: Flowchart of the navigation algorithm.
- Diagram 3: 3D model of the robot structure.
Component Requirements Satisfaction:
- Sensors: Ensure accurate detection of victims and obstacles.
- Microprocessor: Efficiently processes data and controls robot movements.
- 3D Printed Parts: Provide durable and lightweight structural support.
Summary: Through careful planning, role assignment, and iterative testing, our team has developed a comprehensive plan to build and integrate a robot capable of navigating a maze, detecting victims, and earning points according to competition rules. This plan ensures all requirements are met and prepares the team for a successful competition.

#### 3. Hardware
#### High-Level Overview
Our robot is designed with a focus on robust navigation, accurate victim detection, and efficient rescue kit deployment. The hardware design integrates various sensors, cameras, actuators, and a reliable microprocessor to meet competition requirements. Key components include:
- 5 Infrared Sensors: Measure distances to walls and identify checkpoints.
- 1 RGB Color Sensor: Detects black and blue tiles on the floor.
- 2 Cam H7+ Cameras: Identify victims on the walls, communicating via analog signals.
- 2 Limit Switches: Detect collisions.
- 5 Servo Motors: Four for wheel movement and one for the kit dispenser.
These components work together seamlessly to ensure accurate navigation, obstacle avoidance, victim detection, and rescue operations.
#### a. Mechanical Design and Manufacturing
Main Structure: The robot's main structure is a sturdy yet lightweight frame designed to house all components securely. The frame is made of durable materials that can withstand the rigors of the maze environment. The design also allows easy access to all parts for maintenance and upgrades.
Actuators and Power Train: The robot uses four servo motors to drive its wheels, providing precise control over movement and direction. The servo motors are chosen for their high torque and reliability, ensuring the robot can navigate through various obstacles and terrains within the maze.
Subassemblies/Modules: The robot is divided into several subassemblies:
- Navigation Module: Includes the infrared sensors and RGB color sensor for real-time obstacle and tile detection.
- Victim Detection Module: Comprises two Cam H7+ cameras mounted on the sides of the robot to scan walls for victims.
- Collision Detection Module: Utilizes two limit switches placed at the front to detect collisions and trigger avoidance maneuvers.
- Rescue Kit Deployment Module: Features a servo motor-operated dispenser that releases rescue kits near detected victims.
Rescue Kit Deployment Mechanism: The rescue kit deployment mechanism is an innovative design that uses a servo motor to release kits accurately and reliably. This ensures the kits are delivered close to the victims, maximizing points.
Drawings, Diagrams, or Images:
- Diagram 1: Overall layout of the robot's mechanical structure.
- Diagram 2: Detailed view of the rescue kit deployment mechanism.
- Diagram 3: Placement of sensors and cameras on the robot.
Testing Procedures:
- Mechanical Stability Tests: Assess the durability and stability of the robot's frame and components.
- Movement Tests: Ensure the servo motors provide smooth and precise control over the robot's movement.
- Obstacle Navigation Tests: Validate the robot's ability to navigate through ramps, speed bumps, and stairs.
Innovative Solutions:
- Checkpoint Detection: The use of an infrared sensor to identify checkpoints based on distance measurements is an innovative approach that enhances navigation accuracy.
- Infrared Technology for Checkpoints: Utilizing an infrared sensor positioned under the robot to detect checkpoint tiles is a novel solution. When the sensor detects a distance of 200 cm near a checkpoint tile, it accurately marks the location, allowing the robot to save its position effectively.
#### b. Electronic Design and Manufacturing
Sensors Used:
- Infrared Sensors: Five sensors to measure distances to walls and detect checkpoints.
- RGB Color Sensor: Identifies black and blue tiles, aiding in navigation and checkpoint recognition.
- Cam H7+ Cameras: Two cameras for victim detection, providing real-time image data to the microprocessor.
- Limit Switches: Two switches to detect collisions and trigger avoidance maneuvers.
Main Controller: The robot is controlled by an mBot-2 microprocessor, chosen for its educational purpose and powerful processing capabilities. The microprocessor integrates inputs from all sensors and cameras, processes the data, and sends commands to the servo motors.
Power Subsystem: The power subsystem includes a rechargeable battery pack that provides sufficient power for all components. The subsystem is designed to ensure consistent power supply, even during intensive operations.
Drawings, Diagrams, or Images:
- Diagram 4: Schematic of the electronic connections and power distribution.
- Diagram 5: Integration layout showing sensor and actuator connections to the microprocessor.
Testing Procedures:
- Sensor Calibration Tests: Ensure all sensors provide accurate readings.
- Communication Tests: Validate the reliable transmission of data between cameras and the microprocessor.
- Power Consumption Tests: Measure power usage to ensure the battery pack can sustain the robot through the competition.
Innovative Solutions:
- Analog Communication for Cameras: Using analog signals for communication between the Cam H7+ cameras and the microprocessor is an effective solution that simplifies data processing and reduces latency.
- Infrared Technology for Checkpoints: The innovative use of an infrared sensor to identify checkpoint tiles based on specific distance measurements enhances the robot's ability to save and restore its position accurately.
### Summary
The hardware design of our robot incorporates innovative and effective solutions to meet competition requirements. Detailed planning, robust component selection, and thorough testing ensure our robot is well-prepared for the challenges of the maze. The combination of precise navigation, reliable victim detection, and efficient rescue kit deployment makes our robot a strong contender in the RoboCup Junior Rescue Maze competition.
### Software
#### Overview
The robot's software is designed to navigate a maze, detect victims, and efficiently update its internal map to ensure comprehensive exploration. The code logic begins with a button press and follows a structured decision-making process to prioritize movement and obstacle avoidance.
#### a. General Software Architecture
Structure:
1. Initialization:
  1. The robot starts its code upon pressing button A.
  2. Initial configurations and sensor calibrations are performed.
2. Tile Color Check:
  1. The robot first checks the color of the current tile.
  2. If the tile is blue, the robot waits for 5 seconds.
3. Surrounding Check:
  1. The robot checks its surroundings from right to left to identify walls.
  2. If there is no wall, it checks the map to see if the tile has already been visited.
  3. The robot prioritizes movement in the following order: right, front, then left.
4. Decision Making:
  1. If there are no free or unvisited tiles, the robot looks for the nearest tile adjacent to an unvisited tile.
  2. If all tiles have been visited, it calculates the path to return to the starting tile.
5. Movement:
  1. The robot begins moving towards the next tile.
  2. During movement, it continuously checks for blackholes, obstacles, and ramps.
  3. Upon reaching the next tile, the robot updates its map and repeats the process.
Diagrams and Flowcharts:
Flowchart of Main Logic:
You can find the flowchart in the project repo on github.
Integration Problem Solving:
- Obstacle Detection: Continuous sensor readings ensure real-time obstacle avoidance.
- Map Updates: The internal map is updated dynamically to reflect visited tiles and obstacles.
- Priority Movement: The decision-making process prioritizes the exploration strategy to ensure maximum coverage.
#### b. Innovative Solutions
Innovative Approaches:
1. Infrared Checkpoint Detection:
  1. The robot uses an infrared sensor to identify checkpoints based on distance measurements, which enhances navigation accuracy.
2. Dynamic Pathfinding:
  1. If no unvisited tiles are adjacent, the robot dynamically calculates the nearest tile to an unvisited one or plots a route back to the starting point.
Testing Procedures:
1. Sensor Calibration Tests:
  1. Ensured all sensors provide accurate readings before deployment.
2. Obstacle Navigation Tests:
  1. Conducted tests in various maze configurations to validate obstacle detection and avoidance algorithms.
3. Map Accuracy Tests:
  1. Verified that the internal map correctly reflects the maze layout, including visited tiles and identified obstacles.
### Testing of the Code
Every algorithm was rigorously tested on a self-built training ground near our school. We continually optimized the code to achieve the best performance within the shortest possible time.

### Summary
The robot's software architecture combines structured decision-making, dynamic pathfinding, and real-time obstacle detection to navigate the maze effectively. Innovative solutions like infrared checkpoint detection and adaptive waiting times enhance the robot's performance. Comprehensive testing ensures the robot's reliability and efficiency in the competition environment.

### Conclusion
Our team has meticulously designed and developed a robot to compete in the RoboCup Junior Rescue Maze competition. We started by ensuring that our robot could navigate a maze, detect victims, and deploy rescue kits effectively. Key features include a robust hardware setup with multiple sensors, cameras, and servo motors, as well as innovative solutions such as the use of infrared sensors for checkpoint detection.
Each team member contributed significantly to the project. Antonio Saboanu led the software design, leveraging his IT studies to develop the main ideas. Leonardo Padovan, with experience from last year's RoboCup Soccer, focused on programming and hardware integration. Matteo Finotto, also a RoboCup Soccer participant, selected optimal components and ensured efficient cable management. Matteo Uvaldi, with prior experience in the RoboCup Maze, expertly designed and printed the robot’s structure.
Our project plan was well-structured, with clear objectives and milestones. We prioritized tasks based on their dependencies, ensuring a logical flow from mechanical construction to software development. Regular reviews allowed us to track progress and make necessary adjustments.
The software architecture of our robot is built around efficient navigation, obstacle detection, and victim identification. Innovative approaches, such as adaptive waiting times and dynamic pathfinding, were implemented to enhance performance. Rigorous testing on a self-built training ground ensured the reliability and efficiency of our algorithms.
In summary, our comprehensive approach—combining detailed planning, innovative hardware and software solutions, and extensive testing—has prepared our robot to excel in the competition. Each team member's expertise and dedication were crucial in overcoming challenges and achieving our project goals.

References
References to external sources used for major parts of the development process